For those of you just entering 1:8 scale racing. Just a little story about shock-fluids.

In the beginning of the 80's cars were equipped with small shock absorbers 1/4 of the current size. The shock fluid used was normally a kind of transmission oil. 
These oils always changed in viscosity (thickness) during use and temperaturea and a stable shock oil was not there. Therefore all kinds of products were tried. 
Even STP oil was used, you then had to warm up your shocks before racing with a hair dryer before you could use them.
Fortunenatly silicone oil was introduced in the mid 80's. This type of oil has an better constant viscosity over a wider temperature range then other fluids but still is not complete temperature stable!

The thickness of the oil is officially rated in Centi Poise "Cps". 

An other known and used American rating is WEIGHT "WT". 
This WT or W rating is a non world standard and is intriduced by Associated and not comparable between brands using this W or WT rating.

Concerning Cps the thinner the oil (fluid) the lower the number, the ticker the oil the higher the number. 
For normal shock absorber use, this rate may vary between 100 Cps until 900 Cps.
Nowadays we use O-ring sealed diffs, so we can use silicone oil in the diffs instead of thick grease. 
For diffs the rate may vary between 1.000 Cs (loose) up to even 500.000 Cs (very, very, stiff).

Some USA based companies are using the "WT" weight rating, where Japanese and European companies use the better linear industry standard Centi Poise rating. 
A lot off people think that the ratings between the "WT" and "Cps" ratings are linear but this isn't the case.

If there is a factory that can provide oil for testing we can arrange this to see if the product reaches the specification claimed or convert to Cps!

Which manufacturer use which rating?
Which manufacturers you can use same rating oil?
Only manufacturers using Cps as rating are using a world standard and can be mixed used.
Other ratings like W and WT differ from brand from brand as WT or W is not a world standard!

|  | shock oil |
| --- | --- |
| Brand | bottle values | label rating | linear values in Cps |
| Kyosho | 100 - 900 | numbers | yes |
| Mugen | 100 - 900 | numbers | yes |
| Associated | 10 - 80 | WT | no |
| Losi | 10 - 100 | WT | no |
| Orion | 10/100 - 80/800 | numbers | no |
| Xray | 100 - 900 | numbers | yes |
| GS-Racing USA | 20 - 60 | WT | no |
| GS-Racing Europe | 200 - 900 | Cps | yes |
| Crono | ? | ? | ? |
| Serpent | 20 - 50 | W | no |
| Thunder Tiger | ? | ? | ? |
| Trinity | ? | ? | ? |

|  | differential oil |
| --- | --- |
| Brand | bottle values | label rating | linear values in Cps |
| Kyosho | 1.000 - 60.000 | numbers | yes |
| Mugen | 1.000 - 60.000 | numbers | yes |
| Associated | not available | not available | not available |
| Losi | not available | not available | not available |
| Orion | not available | not available | not available |
| Xray | 1.000 - 60.000 | numbers | no |
| GS-Racing USA | 1.000 - 50.000 | Centipoise Cps | yes |
| GS-Racing Europe | 1.000 - 50.000 | Centipoise Cps | yes |
| Crono | ? | ? | ? |
| Serpent | not available | not available | not available |
| Thunder Tiger | ? | ? | ? |
| Trinity | not available | not available | not available |

If you have better information let us know

For shock absorber use, this is the comparison table when using LOSI,  ASSOCIATED and SERPENT some others silicone oil rated in "WT" "W" or are not labeled with a rating but just a number like 30/300

| unofficial conversion values provided by Gene Hickerson USA |
| --- |
| Cps | Losi WT | Associated WT |
| 100 | 10 | 7.5 |
| 150 | 15 | 12.5 |
| 200 | 20 | 17.5 |
| 275 | 25 | 22.5 |
| 300 | 27.5 | 25 |
| 350 | 30 | 27.5 |
| 400 | 32.5 | 30 |
| 425 | 35 | 32.5 |
| 450 | 37.5 | 35 |
| 500 | 40 | 37.5 |

The 50 Cps steps between "Cps" rating are linear, where the 5 "WT" steps used in the "WT" rating are progressive compared to the real thickness of the oil.

No one can tell TEAM TWF8 how "WT" OR "W" rating is measured!!!!! If you know it let us know! info@twf8.ws

| Serpent oil (04-01-2005) |
| --- |
| rating W | Cps |
| 20 | 107 |
| 25 | 207 |
| 30 | 370 |
| 35 | 626 |
| 40 | 1070 |
| 45 | 1449 |
| 50 | 2250 |

We tested this oil supplied by Serpent Benelux on 04-01-2005 in our labaratory and compared them with a calibration oil.of 100 Cps.

Conclusion:
  Serpent oil is way of linear with Cps rating

| Xray silicone oil with Rheometer 09-10-2005 |
| --- |
| Rating | Cps |
| 100 | 106 |
| 150 | 179 |
| 200 | 248 |
| 250 | 292 |
| 300 | 354 |
| 350 | 381 |
| 400 | 441 |
| 450 | 475 |
| 500 | 542 |
| 600 | 625 |
| 700 | 702 |
| 800 | 799 |
| 900 | 913 |
| 1.000 | 1020 |
| Differential usage |  |
| 2.000 | 2490 |
| 3.000 | 4270 |
| 5.000 | 9000 |
| 7.000 | 10500 |
| 10.000 | 13000 |
| 20.000 | 30000 |
| 30.000 | 39600 |
| 60.000 | 65000 |

Use the values above for your benefit and as a guideline.
Xray oil provided by TEAM Xray Slovakia

| Kyosho |
| --- |
| rating | Cps |
| 250 | 244 |
| 300 | 302 |
| 350 | 351 |
| 400 | 411 |
| 500 | 506 |

Use the values above for your benefit and as a guideline.

| Associated silicone oil measured with Rheometer 09-10-2005 |
| --- |
| rating WT | Cps |
| 10 | 108 |
| 15 | --* |
| 20 | 208 |
| 25 | 286 |
| 30 | 373 |
| 35 | 454 |
| 40 | 525 |
| 50 | 707 |
| 60 | 725 |
| 70 | 960 |
| 80 | 1040 |

Use the values above for your benefit and as a guideline.
* The value 15 Weights we measured was like water thickness and is probably a filling fault at the factory.
Altough the contents was silicone oil it was to thin for the 15 WT specs and can not be used for the shocks.
Associated oils were provided by Kendall Bennet from A-mainhobbies and Tony Penzincka from Tony Screws

| Trinity silicone oil measured with Rheometer 09-10-2005 |
| --- |
| rating | Cps |
| 30 | 337 |
| 35 | 376 |
| 40 | 505 |
| 45 | 497 |
| 50 | 658 |
| 55 | 568 |
| 60 | 799 |
| 70 | 757 |
| 90 | 974 |

Use the values above for your benefit and as a guideline.
Trinity oils were provided by Kendall Bennet from A-mainhobbies and Tony Penzincka from Tony Screws

| Losi silicone oil measured with Rheometer 09-10-2005 |
| --- |
| rating | Cps |
| 40 | 576 |
| 45 | 662 |

We did not have all oils from Losi to compared to their own values.
Use the values above for your benefit and as a guideline.
Losi oils were provided by Kendall Bennet from A-mainhobbies and Tony Penzincka from Tony Screws

The only and correct way to measure fluid thickness or to say viscosity is to measure the flow of fluid itself in certain time trough a hole. Simple!

So we do not weigh the weight of the oil as this is a standard value that does not change when the viscosity changes!

A special calibrated measuring device called "Ubbelohde" is a U-tube that contains a certain amount of fluid (in our case the silicone oil). The diameter of the tube and the diameter of the hole where fluid goes through is always constant and calibrated. The thicker the fluid the longer it takes to get a certain amount through. The time the passing of the fluid takes and the known diameter of the hole can produce the figures we need called viscosity.

How does the measurement works?

A vacuum sucks the oil that is in the bottom of the tube up into the front tube. As soon as the top fluid level of the fluid has passed the top (HIGH) sensor the vacuum drops automatically and the oil starts to flow back. A timer is started automatically. As soon as the the fluid level passes the other sensor (LOW) the time counting is stopped! The time it takes for the level to go from the high to the low sensor is the time we need to calculate the viscosity of the fluid.
As we know the amount of oil, the time it takes and the diameter of the calibrated hole we can calculate the viscosity in mm²/s. Then we have the viscosity in Centistokes value.
Centi Poise (nowadays called Pascal per second) is the result of the Centistokes value magnified with the density of the oil.
Normally for silicone oil this value is 0.9875 = almost 1.0

To perform the whole measurement accurate and constant we have to calibrate the whole system first. Normally this is done when the tube is placed in a water bath that is keeping the whole measurement set up on same temperature @ 22 degrees Celsius for the whole measurement. A calibration fluid is used to check if the reading is correct or need to be adjusted before the real measurement takes place.
Then the tested oil is placed into the tube and the test is performed. As not all oils are the same in viscosity, there are different tubes with a calibrated hole to get the appropriate and corresponding readings.

From September 2006 we measure all oils with a RHEOMETER.

SILICONE SHOCK OIL AND TEMPERATURE

Although everybody thinks silicone oil is not affected by temperature, we can wake you up out of that dream. 
When the same test is done @ 12 or @ 32 degrees Celsius we get other values!
Test result from the Albemarle laboratories provided us with the following fist rule:

When temperature is 10 degrees Celsius lower or higher the viscosity decreases or increases by 5%. Example:

200Cps @ 12 degrees Celsius is 210 Cps
200Cps @ 22 degrees Celsius is 200 Cps
200Cps @ 32 degrees Celsius is 190 Cps

Team TWF8 special thanks goes to Jacco Koch our Chemicals specialist from The Netherlands for testing the fluids and the pictures.

Click here and see how to mix your silicone shock and diff oils in the right percentages.