*********************************************************************************************

2011-10-8

The Firmware database of the car ESC has been updated to the latest Version 111008.

- Two new firmwares named “V3.0_110930_MOD” and “V3.0_110930_STOCK” are available for the following ESC’s:

XERUN-120A (V2.0), XERUN-60A (V2.0), XERUN-120A (V2.1), XERUN-60A (V2.1), Xtreme STOCK

  - “V3.0_110930_MOD” is an improved firmware version based on “V3.0_110119_MOD”; the new firmware has been updated to improve the fault tolerance of the signal quality of the Hall sensors within the sensor board of brushless motors. 
The old firmware was found to be too sensitive to any small change of the sensor signal, in turn causing the ESC to frequently switch its running mode from sensored to sensor less sensor signal. The new firmware is not as sensitive, so the ESC can still operate in sensored mode even if the signal has slight changes in amplitude from small errors that might eventuate this will help Mod motors which have very large current flows which cause the signal within the motor sensor board of the motor to change frequently causing unnecessary errors .

  - “V3.0_110930_STOCK” is a new version based on “V3.0_110211_STOCK”, same improvements as above.

- New firmware named “V3_508_No Timing” is also available for the JUSTOCK ESC. The improvements are as follows:

  - The “Maximum Brake Force” has been increased from 4 options to 8 options for finer adjustment.

  - The new firmware has also been improved for fault tolerance of the signal quality of the Hall sensors within the sensor board of the brushless sensored motor’s.