Kyosho Spring Chart

IS106 series are 84mm long and are used on ST-R, ST-RR front and MP9 rear.

softer

-Is106-9514 - yellow - 9.5 turns of 1.4mm wire

-is106-914 - green - 9 turns of 1.4mm wire

-is106-1116 - white - 11 turns of 1.6mm wire

-is106-8514 - orange - 8.5 turns of 1.4mm wire

-is106-1016 - purple - 10 turns of 1.6mm wire

-is106-814 - light blue - 8 turns of 1.4mm wire

-is106-916 - light green - 9 turns of 1.6mm wire

-is106-816 - blue - 8 turns of 1.6mm wire

harder

if350 series are 70mm long and used on the MP9 front

softer

-if350-1016 - white - 10 turns of 1.6mm wire

-if350-814 - green - 8 turns of 1.4mm wire

-if350-7514 - orange - 7.5 turns of 1.5mm wire

-if350-916 - purple - 9 turns of 1.6mm wire

-if350-6514 – gray – 6.5 turns of 1.4mm wire

-if350-714 - light blue - 7 turns of 1.4mm wire

-if350-816 - light green - 8 turns of 1.6mm wire

-if350-716 - blue - 7 turns of 1.6mm wire

harder

if348 series are 95mm long and used on the rear of the ST-R, ST-RR, and MP777

softer

-if348-1114 - green - 11 turns of 1.4mm wire

-if348-1316 - white - 13 turns of 1.6mm wire

-if348-1014 - light blue - 10 turns of 1.4mm wire

-if348-1216 - purple - 12 turns of 1.6mm wire

-if348-1116 - light green - 11 turns of 1.6mm wire

-if348-1016 - blue - 10 turns of 1.6mm wire

-if348-916 - red - 9 turns of 1.6mm wire

harder