Additional Instruction of 110108_STOCK Firmware

Note! The 110108_STOCK firmware is NOT identical with the 1224_STOCK firmware.

Compared with the previous versions such as 0518_STOCK, the 3rd generation STOCK firmware of “110108_STOCK” has the following improvements:

- Stronger and quicker acceleration, but the temperature of ESC and motor is even lower than before.

- Boost Timing and Turbo Timing can be adjusted more smoothly, with the precision of 1 degree per step.

- Turbo Timing and Boost Timing can be composited to be functional together (Total effective timing is 30°).

- Turbo Timing increasing rate (slope rate) is adjustable.

- Brake Force is changed from 4 options to 8 options.

Caution!

- Once the new firmware has been loaded into the ESC, you can only use the LCD Program Box or PC software to set the programmable parameters, neither the LED Program Card nor the SET button is available for programming the ESC with this new firmware.

- You must update the firmware of the LCD Program Box to Version “101224” to be compatible with the new firmware of ESC.

How to update the firmware of the LCD program BOX?

Please check here: http://www.hobbywing.com/upload/manual/USB_LINK_User_Manual.pdf

Description of the programmable items about Turbo function

#9.Boost Timing：It refers to the normal timing which is effective throughout the entire throttle range and affects the motor speed in the entire track (Curve and straight track). Please note this refers to the maximum value of the ESC internal timing, the actual timing is always dynamically changed every moment according to the motor RPM.

| Boost Timing (Degree) | 0° to 30° with the trim step of 1° |
| --- | --- |

#10、Turbo Slope Rate (Degree/0.1s). This refers to the Turbo Timing increasing rate. The higher it is, the faster the Turbo Timing increases, and together with a quicker acceleration and higher motor temperature.

| Item | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Turbo Slope Rate (Degree/0.1s) | 1.5°/0.1s | 3°/0.1s | 6°/0.1s | 9°/0.1s | 12°/0.1s | Full Turbo Timing opened immediately |

Example: Turbo Timing is set to 12°and Turbo Slope Rate is set to 1.5°/0.1s, it takes 0.8S to activate this 12°Turbo Timing.

＃12、Turbo Timing：It is the additional timing that added to the Boosting Timing and ONLY effective when the throttle is fully opened, so usually it is useful for long straight track.

| Turbo Timing (Degree) | 0° to 12° with the trim step of 1° |
| --- | --- |

The maximum amount of timing (Boot Timing + Turbo Timing) of the ESC is designed to 30°. If the sum of “Boost Timing + Turbo Timing” is more than 30°, only 30° is effective and the exceeding value is useless.

Example 1:

Boost Timing set to 30°, Turbo Timing set to 10°

30° timing can be activated before the throttle is fully opened, but no more timing can be activated even if the throttle is fully opened.

Example 2:

Boost Timing set to 25°, Turbo Timing set to 10°

25° timing can be activated before the throttle is fully opened, and the further 5° timing can be activated when the throttle is fully opened.

＃13、Boost Start RPM： ESC begins to increase the internal timing when motor speed reaches the Boost Start PRM. A smaller Boost Start RPM value causes a faster rate of boost because the ESC increases the internal timing earlier.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Motor speed (RPM) | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 12000 |

＃14、Turbo Delay： This is the amount of time “full throttle” must be held BEFORE the turbo function engages. If the full throttle time is less than the setting value, the turbo function will NOT be activated.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Time(s) | 0s | 0.1s | 0.2s | 0.3s | 0.4s | 0.5s | 0.6s | 0.7s | 0.8s |

＃15、Boost Timing Acceleration：This refers to the RPM increment that triggers the Boost Timing increase of 1 Degree. The lower value it is, the punchier the motor will be but conversely the hotter the motor will get.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Boost Timing Acceleration（RPM/Degree） | 150 | 250 | 350 | 450 | 600 | 750 | 900 |

This parameter is often misunderstood. The boost timing change is caused by the RPM increment, so we use this Boost Timing Acceleration parameter to control the increasing rate of Boost Timing.

So the change of RPM is the cause and the change of Boost Timing is the effect.

Generally, the larger the timing you set, the more powerful the motor will be, but hotter the motor will get. The motor may over-heat or even smoke if too much of timing is activated when a motor is running at a low speed. In order to solve the problem, we use the method of dynamic timing. The motor gets small amount of timing in the period of low speed, when the motor speed reaches the Boost Start PRM, then the timing begins to increases together with the RPM.

| The Relationship between Speed and Timing |
| --- |
| Example 1 Boost Start RPM = 4000 Boost Timing Acceleration =350/degree | Example 2 Boost Start RPM =9000 Boost Timing Acceleration =600/degree |
| Speed（RPM） | Timing | Speed (RPM) | Timing |
| <4000 | 0 | <9000 | 0 |
| 4350 | 1 | 9600 | 1 |
| 4700 | 2 | 10200 | 2 |
| 5050 | 3 | 10800 | 3 |
| 5400 | 4 | 11400 | 4 |
| 5750 | 5 | 12000 | 5 |
| 6100 | 6 | 12600 | 6 |
| 6450 | 7 | 13200 | 7 |
| 6800 | 8 | 13800 | 8 |
| 7150 | 9 | 14400 | 9 |
| 7500 | 10 | 15000 | 10 |
| 7850 | 11 | 15600 | 11 |
| 8200 | 12 | 16200 | 12 |
| 8550 | 13 | 16800 | 13 |
| 8900 | 14 | 17400 | 14 |
| 9250 | 15 | 18000 | 15 |
| 9600 | 16 | 18600 | 16 |
| 9950 | 17 | 19200 | 17 |
| 10300 | 18 | 19800 | 18 |
| 10650 | 19 | 20400 | 19 |
| 11000 | 20 | 21000 | 20 |
| 11350 | 21 | 21600 | 21 |
| 11700 | 22 | 22200 | 22 |
| 12050 | 23 | 22800 | 23 |
| 12400 | 24 | 23400 | 24 |
| 12750 | 25 | 24000 | 25 |
| 13100 | 26 | 24600 | 26 |
| 13450 | 27 | 25200 | 27 |
| 13800 | 28 | 25800 | 28 |
| 14150 | 29 | 26400 | 29 |
| 14500 | 30 | 27000 | 30 |
| >14850 | 30 | >27600 | 30 |

Caution: If the setting value of “Boost Timing” is less than 30°, for example, set to 20°, the Timing will be still 20° even if the motor speed is higher than 11000RPM in example 1.

Summary:

- The way to get a higher top speed:

- Increase Timing

- Reduce FDR

- Increase acceleration

- The way to increase the start acceleration:

- Increase Timing

- Reduce Boost Start RPM or reduce Boost Timing Acceleration

- Increase FDR

- Reduce Turbo Delay

- Increase Turbo Slope Rate

- Increase Start Punch (This is the programmable item #4 of the ESC, please check the user manual of the ESC)

- The way to decrease motor temperature and get a longer running time:

- Reduce Timing

- Increase Boost Start RPM or increase Boost Timing Acceleration

- Increase Turbo Delay

- Reduce Turbo Slope Rate

The table below is a recommended setting list. (2 cells Lipo, Motor endbell physical timing is 0° to 5°)

| Car | Motor | FDR | ＃9 Boost Timing | #10 Turbo Slop Rate | ＃12 Turbo Timing | ＃13 Boost Start RPM | ＃14 Turbo Delay | ＃15 Timing ACC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1/10 On-Road | 11.5T | 5.7-6.8 | 20° | 9°/0.1s | 8° | 2000 | 0.4 | 750 |
|  | 13.5T | 5.0-7.0 | 23° | 9°/0.1 s | 10° | 4000 | 0.4 | 450 |
|  | 17.5T | 5.0-7.0 | 25° | 9°/0.1 s | 10° | 3000 | 0.2 | 250 |
| 1/10 Off-Road (Normally, turbo function is NOT recommended for Off-Road car) | 11.5T | 7.5-9.5 | 6° | 3°/0.1 s | 2° | 6000 | off | 600 |
|  | 13.5T | 7.0-9.0 | 8° | 3°/0.1 s | 4° | 5000 | off | 450 |
|  | 17.5T | 7.0-8.5 | 10° | 3°/0.1 s | 6° | 3000 | off | 250 |

The FDR depends on the track condition. Generally, gearing down to get a higher top speed in the large track with long straight, or gearing up to improve the punch out of the corner in the small track.