Additional Instruction For 1224_STOCK Firmware

Compared with the previous versions, the 3rd generation STOCK firmware of “1224_Stock” has the following improvements:

- Stronger and quicker acceleration, but the temperature of ESC and motor is even lower than before.

- The Boost Timing and Turbo Timing can be adjusted more smoothly, with the precision of 1 degree per step.

- The Turbo timing and boost timing can be composited to be functional together.

- Turbo timing increasing rate (slope) is adjustable.

- Brake Force is changed from 4 options to 8 options.

Caution!

- Once the new firmware has been loaded into the ESC, you can only use the LCD Program Box to set the parameters of the ESC.

- You need to update the firmware of the LCD Program Box to compatible with this firmware.

How to update the firmware of the LCD program?

Please check here: http://www.hobbywing.com/upload/manual/Hobbywing%20USB%20Link%20manual.pdf

Description of the programmable items about Turbo function

#9.Boost Timing：（More effective when larger torque is needed）It is effective throughout the entire throttle range and affects the motor speed in the entire track (Curve and straight track). Please note this refers to the maximum value of the ESC internal timing, the actual timing is always dynamically changed every moment according to the motor RPM.

| Actual Max Timing (Degree) | 0°to 38°with the trim step of 1° (The actual max Boost Timing is 30°. If the setting value is more than 30°, the Turbo Timing will be functional with the first priority ) |
| --- | --- |

#10、Turbo Slope Rate (Degree/0.1s). This refers to the Turbo Timing increasing rate. The higher this parameter, the shorter time Turbo Timing increase, and together with a quicker acceleration and higher motor temperature.

| Item | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Turbo Slope | 1.5°/0.1s | 3°/0.1s | 6°/0.1s | 9°/0.1s | 12°/0.1s | All Turbo Timing opened immediately |

Example: Turbo Timing is 12°and Turbo Slope is 1.5°/0.1s, it takes 0.8S to activate the whole Turbo Timing.

＃12、Turbo Timing：（More effective when quicker motor speed is needed）.It is the additional timing that added to the Boosting Timing and only effective when the throttle is fully opened, so usually it is useful for long straight track.

| Actual Max Timing (Degree) | 0°to 30°with the trim step of 1° (The actual max value is 16°. If the Boost Timing is less than 30°,the Turbo Timing compensate the section as Boost Timing first, the rest is the actual Turbo Timing. For example, Boost Timing is 16°and Turbo Timing is 30°, 14°will be Boost Timing and 16°be Turbo Timing after full throttle is held. If Boost Timing is 30°and Turbo Timing is 30°, the actual Turbo Timing is 16°) |
| --- | --- |

＃13、Boost Start RPM： ESC begins to increase the internal timing when motor speed reaches the Boost Start PRM. A lower Boost Start RPM setting will produce a faster rate of boost because the ESC increases the internal timing earlier.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Motor speed (RPM) | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 12000 |

＃14、Turbo Delay： This is the amount of time ‘full throttle’ must be held BEFORE the turbo function engages. If the fully opened time of throttle is less than the setting value, the turbo function will NOT be activated.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Time(s) | 0s | 0.1s | 0.2s | 0.3s | 0.4s | 0.5s | 0.6s | 0.7s | 0.8s |

＃15、Boost Timing Acceleration：This refers to the RPM increment that triggers the ESC timing increase of 1 Degree. The lower you set this the punchier the motor will be but conversely the hotter the motor will get.

| Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Timing Acceleration（RPM/Degree） | 150 | 250 | 350 | 450 | 600 | 750 | 900 |

Physically, the actual max timing of (Boost Timing + Turbo Timing) is 46°. If the summation of the setting values is more than 46°, only 46°is functional and the exceeded degree is useless.

The higher the timing you set, the more powerful the motor will be, but the hotter the motor will get. The motor will be over-heat or even smoke if too much of timing is activated when a motor is running at a low speed. In order to solve the problem, we take the method of dynamic Timing. The motor gets small amount of timing in the period of low speed, then the timing increases together with the speed after the motor reaches a higher speed. The Timing refers to the motor speed can be adjusted by adjusting the Boost Start RPM and Boost Timing Acceleration.

| The Relationship between Speed and Timing |
| --- |
| Example 1： Boost Start RPM = 4000， Boost Timing = 38° Boost Timing Acceleration =350/degree | Example 2： Boost Start RPM =9000， Boost Timing = 38° Boost Timing Acceleration =600/degree |
| Speed（RPM） | Timing | Speed (RPM) | Timing |
| <4000 | 0 | <9000 | 0 |
| 4350 | 1 | 9600 | 1 |
| 4700 | 2 | 10200 | 2 |
| 5050 | 3 | 10800 | 3 |
| 5400 | 4 | 11400 | 4 |
| 5750 | 5 | 12000 | 5 |
| 6100 | 6 | 12600 | 6 |
| 6450 | 7 | 13200 | 7 |
| 6800 | 8 | 13800 | 8 |
| 7150 | 9 | 14400 | 9 |
| 7500 | 10 | 15000 | 10 |
| 7850 | 11 | 15600 | 11 |
| 8200 | 12 | 16200 | 12 |
| 8550 | 13 | 16800 | 13 |
| 8900 | 14 | 17400 | 14 |
| 9250 | 15 | 18000 | 15 |
| 9600 | 16 | 18600 | 16 |
| 9950 | 17 | 19200 | 17 |
| 10300 | 18 | 19800 | 18 |
| 10650 | 19 | 20400 | 19 |
| 11000 | 20 | 21000 | 20 |
| 11350 | 21 | 21600 | 21 |
| 11700 | 22 | 22200 | 22 |
| 12050 | 23 | 22800 | 23 |
| 12400 | 24 | 23400 | 24 |
| 12750 | 25 | 24000 | 25 |
| 13100 | 26 | 24600 | 26 |
| 13450 | 27 | 25200 | 27 |
| 13800 | 28 | 25800 | 28 |
| 14150 | 29 | 26400 | 29 |
| 14500 | 30 | 27000 | 30 |
| 14850 | 31 | 27600 | 31 |
| 15200 | 32 | 28200 | 32 |
| 15550 | 33 | 28800 | 33 |
| 15900 | 34 | 29400 | 34 |
| 16250 | 35 | 30000 | 35 |
| 16600 | 36 | 30600 | 36 |
| 16950 | 37 | 31200 | 37 |
| 17300 | 38 | 31800 | 38 |
| >17300 | 38 | >31800 | 38 |

Caution: If Boost Timing is less than 38°,such as 20°, the Timing will be still 20°when the motor speed is higher than 11000 in example 1.

总结：The punch out of the corners is improved

Summary:

（1）.	The way to get a higher top speed:

- Increase Timing

- Reduce FDR

- Increase acceleration

（2）.	The way to increase the start acceleration:

- Increase Timing

- Reduce Boost Start RPM or Boost Timing Acceleration

- Increase FDR

- Reduce Turbo Delay

- Increase Turbo Slope

- Increase Start mode

（3）.	The way to decrease motor temperature and get a longer running time:

- Reduce Timing

- Increase Boost Start RPM or Boost Timing Acceleration

- Increase Turbo Delay

- Reduce Turbo Slope

The table below is a recommended setting for you. (2 cells Lipo, Motor endbell Timing is 0° to 5°)

| Car | Motor | FDR (Gera ratio) | ＃9 Boost Timing | #10 Turbo Ramp | ＃12 Turbo Timing | ＃13 Boost Start RPM | ＃14 Turbo Delay | ＃15 Timing ACC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1/10 On-Road | 11.5T | 5.5-7.0 | 26 | 9°/0.1s | 16 | 7000 | 0.4 | 600 |
|  | 13.5T | 5.0-7.0 | 30 | 9°/0.1 s | 16 | 4000 | 0.4 | 450 |
|  | 17.5T | 5.0-7.0 | 38 | 9°/0.1 s | 16 | 3000 | 0.2 | 250 |
| 1/10 Off-Road (Normally, turbo function is NOT recommended for Off-Road car) | 11.5T | 7.5-9.5 | 8 | 3°/0.1 s | 4 | 6000 | off | 600 |
|  | 13.5T | 7.0-9.0 | 10 | 3°/0.1 s | 6 | 5000 | off | 450 |
|  | 17.5T | 7.0-8.5 | 12 | 3°/0.1 s | 8 | 3000 | off | 250 |

The FDR depends on the track condition. Gearing down to get a higher top speed in the large track with long straight, while gearing up to improve the punch out of the corner in the small track.